## Slide 1
Using distributed solvers in UG Utz-Uwe Haus, Yuji Shinano
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 773897.

## Slide 2: Vision
Enable UG to
  Use multi-rank MPI-based solvers
    with varying size over the course of the run
    possibly from heterogeneous set of solvers
Why?
  Single-rank may simply not be enough
  Scalable solver codes may realize a subproblem needs more resources and want to be restarted in a different size
    Not all subproblems readily decompose into ‘new nodes’ for UG to collect
    May permit to alleviate resource shortage (memory!) of a subsolver
  Experiments with dynamic solver resource allocation
    API design for the solver library used in

## Slide 3: UG solver interface
Traditionally every MPI-parallelized solver subclasses class UG::ParaCommMpi
Alternative: class UGS::UgsParaCommMpi
UGS::UgsParaCommMpi encapsulates world, solver, and master+solver communicators
  Feature in UG 0.8.6, use UGS=true in Makefile
  Used in MPMD multi-solver setup
    Used in parallel heuristic code ugs_pacs_xpress
    Can even run UG solvers as sub-solvers
  Other solvers currently do not make use of multiple ranks per solver

## Slide 4: Revisiting an old, new solver: Concorde
Still one of the best TSP-codes
  D. Applegate, R. Bixby, V. Chvátal, and W. Cook
    http://www.math.uwaterloo.ca/tsp/index.html
Written in C
  Pretty clean code base
  LP solver can be cplex or qsopt
  Needs good starting solutions for harder problems
    Column generation relies on never generating more than columns
Can be built in a TCP-socket based multi-node version
  Hard to use, not documented

## Slide 5: Concorde on HPC
Directly after porting to MPI
  Simple MPI rank based process partitioning:
    Dedicate rank 0 to “boss” process
    Dedicate remaining ranks to be “grunt” (=worker”) processes
    Could also dedicate cut server or heuristic nodes
  Replace TCP communication by MPI rank-to-rank Send/Recv
    Low communication demands (size and frequency)
Using Cray cluster-compatibility-mode
  A Cray module that permits allocation of nodes to behave like a cluster
  Each process (“boss”, “grunt”, …) needs to be started individually
  No way we could reasonably script this to become a UG solver class

## Slide 6: UG[Concorde/MPI,MPI]
UG solver talks to rank 0 (“boss”) of Concorde/MPI
Random seed has large influence on Concorde runs
  Multiple different seeds from UG are a good heuristic to get started
Concorde starts with columns generation on rank 0, only uses additional ranks when doing B&B
  We currently have no good way of guessing the right process size a priory
  Need to implement a feedback mechanism to UG to ask for ‘restart this subproblem with more B&B nodes’
    Needs to be weighted against the option of simply passing back all subproblems to UG and running single-rank Concorde

## Slide 7: State and Goal
Goal
UG orchestrating
  multiple Concorde/MPI instances, cut servers, heuristic instances
    Starting small runs
    Collecting nodes
    Handling “Could use more ranks” messages, dynamically re-running such nodes
Data exchanged using universal data exchange library, not Files or explicit MPI
  UDJ, a CERL project, developed within
Today
Can run single-rank Concorde inside UG
  Files with node and cut information used to transfer subproblem information
  Concurrency issues, file naming issues, IO bottleneck
Can run Concorde/MPI with hundreds of ranks
  Concorde slow to generate subproblems
  TSPlib problems mostly solved in root
Integration ongoing

## Slide 8: The dynamic MPI worker resource allocation problem
Master
idle ranks
Master
Solver 1
Solver 2
idle ranks

## Slide 9: The MPI worker resource allocation problem
Master
Solver 1
Solver 2
idle ranks
Master
Solver 1
idle ranks
idle ranks
Solver 3
Solver 2 terminates,
Solver 3 started:
Issues:
Useful size estimation
Fragmentation of free ranks
  Luckily MPI does not care
  but rank placement influences performance

## Slide 10: The gory parts: Dynamic MPI groups
Most people use MPI in one of the following modes
  MPI_COMM_WORLD – MPI provides a way for all ranks to communicate
    Master (rank 0)/worker (rank!=0) paradigm like in UG[*,MPI]
    Distributed data, rank number carries index information
  MPI_Comm_split() – Application splits MPI_COMM_WORLD at program start to create multiple (independent) multi-rank applications
    Each group used like above
    Groups can talk to each other through original MPI_COMM_WORLD or (less common) through MPI-DPM
  MPI_Group_create() – Application creates groups of logically related ranks, one rank may be in multiple groups
    E.g., distributed tensorial data with groups for slices sharing one or more index dimensions

## Slide 11: The gory parts: Dynamic MPI groups (2)
Collective vs. Non-Collective communicator creation
  MPI_Comm_split() is collective
  MPI_Comm_create_group() is collective only over the group
    The group can be created using MPI_Group_incl(), which is a local operation on each rank
So the protocol can be
  Master rank 0 selects worker rank set S
    Master sends ranks in S ‘form_group(S)’ message
    Each rank in S do MPI_Group_incl(WORLD_GROUP,S,&G(S))
    Master and each rank in S do MPI_Group_incl(WORLD_GROUP,, &M(S))
    Each rank in S does MPI_Comm_create_group() to obtain the C(S) communicator
    Master and each rank in S do MPI_Comm_create_group() to C() communicator
  C(S) communicator is used for distributed solver
  C() communicator is used for master-worker communication
    Possibly a dedicated rank or set of ranks in S does the communication with the master rank
  When distributed solver is done:
    C(S) and C(), and G(S), and M(S) are destroyed

## Slide 12: Data transfer between subsolvers
Currently file-based

## Slide 13: Summary
UG can already pass an MPI communicator to your solver (UGS superclass)
We’ll work on a simplistic resource (=rank) allocation toolset
There’s a nice optimization problem hiding here
  K-machine job scheduling, plus
  Communication-aware rank subset selection
    Depends on having communication model for the solver
  Solver scaling choices: more smaller or fewer bigger solvers?

## Slide 14
  Utz-Uwe Haus, uhaus@cray.com
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 773897.